## Slide 1: HW3: Hardware Implementation of Single Cycle RISC-V
Speaker: Kane
Instructor:吳安宇教授
Date: 2021/04/08
Digital System Design

## Slide 2
Homework 3
Single-cycle RISCV Processor

## Slide 3: Problem Statement
Using Verilog, implement the single-cycle RISC-V processor:
  Supported instructions:
    add, sub, and, or, slt
    lw, sw
    beq
    jal, jalr
Most specifications are the same
(Bonus) Compressed-Instruction(p.11)

## Slide 4: Block Diagram(1/2)
Instruction ROM:
contains the testing instructions
Data Memory:
contains the stored data
  Used for testing your circuit
mem_wen_D:
mem_wen_D is high, writing data to D-mem when the next clk arrive; else reading
data from memory to chip.

## Slide 5: Block Diagram(2/2)
mem_addr_I
mem_rdata_I

## Slide 6: Testbench
The testbench will
  Initialize the instruction rom and the data memory
  Reset your circuit
  Execute the instructions, and check the values stored in data memory to see whether your circuit is correct
  If your function is correct, you will see the following

## Slide 7: Clock/Reset/Register File
Clock: positive edge triggered
Reset: active low synchronous reset
Register file
  All registers are reset to 0 when reset occurs
  Register x0 must be always 0
There is no endianness issue!
  If you store 32’h12345678 in x8, RF_8_w[31:0] = 32’h12345678

## Slide 8: Memory Layout
Instruction memory for RISC-V
Data memory for RISC-V
Conversion between big/little-endian
  out[31:0] = {in[7:0], in[15:8], in[23:16], in[31:24]};

## Slide 9: Memory
Instruction ROM and data memory are included in the testbench
As for data memory
  32 words x 32 bits
  The input signal mem_wen_D is high, writing data to D-mem when the next clk arrive; else reading data from memory to chip.

## Slide 10: Memory Addressing
In RISCV, the memory address is byte address.
In Instruction ROM and data memory , the memory address is word address.
Both the memory size of Instruction ROM and data memory in this work are 32x32, so their input address is 5-bit wide.
  You are encouraged to observe the connection between each module in RISCV_tb.v .

## Slide 11: (Bonus) Compressed-Instruction
Your RISCV also needs to support 16-bit compressed instructions.
One of the suggestion is creating a decompressor module to distinguish whether the inst. is compressed or not. Recovering the 16-bit inst. to 32-bit inst. by 1-1 mapping, and then processing as usual.
  Supported instructions:
    C.add, C.sub, C.and, C.or
    C.lw, C.sw
    C.beqz
    C.jal, C.jalr
  Use +define+RTL+RV32IC / +define+SYN+RV32IC to test
  More information: Introduction_to_RISCV_C-extension&implementation.pptx

## Slide 12: Block Diagram
Instruction ROM:
contains the testing instructions
Data Memory:
contains the stored data
  Used for testing your circuit
decompressor:
  Resolve the raw inst. from I-ROM and output the correct mem_rdata_I to CHIP
  Maintain the PC and output the correct address to fetch inst. from I-ROM

## Slide 13: Simulation & Synthesis
Check “RISCV/ verilog/ readme.txt”
3 Major Things
  RTL coding & simulation
  Logic Synthesis
  Gate-level simulation & debugging/refinement
Files needed for simulation
  RTL code: CHIP.v
  Gate-level code: CHIP_syn.v
  Timing info (SDF file): CHIP_syn.sdf
  Design library (DDC file): CHIP_syn.ddc

## Slide 14: ※Notice
Latches are not allowed in gate level code after synthesis, use Flip-flop instead.
Negative Slack and Timing Violations are not allowed after synthesis.
The tsmc13.v file is not allowed to be downloaded! Or you may offend the copyright protected by NTU & CIC!

## Slide 15: Grading Policy
RTL (40%): function correctness
Synthesis (30%): correctness
Report (10%)
Area*Timing (20%)
TA: 蔡文喬
daniel@access.ee.ntu.edu.tw
TA: 馬咏治
kane@access.ee.ntu.edu.tw

## Slide 16: Report
Simulated timing (ns)
  Gate-level simulation clock cycle
  (i.e. The cycle you passed testbench after synthesis)
Area(um^2)
  report_area
Cost(A*T)
  Area*Gate-level simulation clock cycle
ScreenShot
  Inferred memory devices in process
  (※No latch should be inferred!)
Area
Timing

## Slide 17: Submission(1/2)
For each topic, you need to submit 4 files + 1 report
  RTL code: CHIP.v
  Synthesis:
  CHIP_syn.v,
  CHIP_syn.sdf,
  CHIP_syn.ddc
  Report: report.pdf
Compress all the files into one ZIP file
  File name: DSD_HW3_學號.zip
  EX: DSD_HW3_b06901001.zip
Upload the file to Ceiba
Deadline: 2021/04/29 24:00 ※Late submission is not allowed

## Slide 18: Submission(2/2)
DSD_HW3_學號/
RISCV/
CHIP.v
CHIP_syn.v
CHIP_syn.sdf
CHIP_syn.ddc
(optional)
CHIP_RV32IC.v
CHIP_RV32IC_syn.v
CHIP_RV32IC_syn.sdf
CHIP_RV32IC_syn.ddc
MIPS/ (Optional)
CHIP.v
CHIP_syn.v
CHIP_syn.sdf
CHIP_syn.ddc
report.pdf

## Slide 19: Appendix A
Why Little endian?
  Fetch with the same address if a given value is stored in different width
    32bit 0x0D0C0B0A
    64bit 0x000000000D0C0B0A
    We can always fetch the lowest 32bit address
  Mainstream
    Intel x86